## Slide 1: TRANSIMS Version 5 Application Concepts
January 20, 2011
David Roden – AECOM

## Slide 2: Topics
Goals and objectives
NetPrep applications
Router applications
PathSkim applications
Microsimulator applications
Resent convergence discussions

## Slide 3: Goals and objectives
Improve user interaction during network conversion
  Separate link selection and collapsing from relational file generation
Streamline the application process
  Consolidate processing steps
  Minimize the number intermediate/working files (e.g., plan files)
Coordinate partitioned tasks to cumulate shared and dependent data (e.g., flow and travel times)
  Performance statistics and reports based on all partitions
Improve performance and functionality for demand model feedback (i.e., skims)

## Slide 4: Version 4 Network Preparation
Convert source data  link and node files
  GISNet, TPPlusNet, EMME2Net, TransCAD GISDK
    Develop a User Program script to manipulate link data fields
  Review and edit link and node files
Synthesize TRANSIMS network with TransimsNet
  Review network, refine parameters, re-run
    Manually edit or provide Update/Delete commands
  Review and edit signal and sign warrants
Synthesize traffic controls with IntControl
  Coordinate signal offsets with Progression
(Similar process for transit networks)

## Slide 5: Version 5 Network Preparation
Convert and edit source data  link and node files
  NetPrep (input GIS, TP+, EMME/2, TRANSIMS network files)
    Develop a User Program script to manipulate link data fields
    Merge, select and collapse nodes and links
    Apply Update/Delete commands
  Review and edit link and node files
Synthesize TRANSIMS network with TransimsNet
  Review network, refine parameters, re-run
  Apply Update/Delete commands
  Review and edit signal and sign warrants
Synthesize traffic controls with IntControl
  Coordinate signal offsets with Progression

## Slide 6: Network Preparation Differences
Greater focus on the initial develop of the input link and node file
  Additional data manipulation and update/delete tools
  Tools for selecting a subset of links from an all-streets network
TransimsNet includes much finer controls of synthetic data generation
  Pocket lanes, link connections, activity locations, traffic controls, parking details, speeds, and other attributes

## Slide 7: Router Applications
Additional path building controls and features
  Forward or backward path building with trip end constraints
  Expanded selection criterion
    Time, location, zone, traveler type, mode, household, etc.
    Build paths for individual travelers or trips within a household
  More rigorous path building algorithm available to minimize transit transfer anomalies
  Parking and vehicle operating costs included in path building
    Can be varied by vehicle type
  Traveler type script for traveler-specific path building parameters
  Local impedance factor to avoid hard-limit effects

## Slide 8: Router Performance Enhancements
Faster and integrated Router-based iterations
  Create link-delays directly from Router
    Independently control update of link flows and link travel-times
    Build upon input flows / travel-times or start from free-flow conditions
    Choice of periodic update vs. single final update
  Multi-step incremental loading can be replaced with single application
  PlanSum can be bypassed
  Integrated Plan merging (PlanPrep)
    Subset of input plans can be replaced with selective re-routing/update

## Slide 9: Version 4 Router Applications
Router
Plans.*
PlanSelect
HHList.*
PlanSum
LinkDelay
PlanPrep
TravelPlans.*
LinkDelay
Trip File
TravelPlans.*

## Slide 10: Version 5 Router Applications
Router
PlanSelect
Select.*
LinkDelay
TravelPlans.*
LinkDelay
Trip File
TravelPlans.*

## Slide 11: Version 4 Travel Skims
Router + PlanSum
  Enter a list of origin and destination Activity Locations
  Set start time increments
  Build a plan for each O-D-T
    Long run times
    Huge plan files
  Use PlanSum to summarize the plans and aggregate zone or district skims
    Limited O-D-T index size
  Single output skim file
Router
Plans
PlanSum
Zone Skim
Select O-D-Ts
Link Delays

## Slide 12: Version 5 Travel Skims
PathSkim
  Multiple methods for automatically selecting origins and destinations
  Multiple or merged variable length time periods
    Start or end time points
  One-to-many path building and save only skim data
    No need to write/read plans
  Location/zone/district skims
  Multi-threading and time-period based partitioning
PathSkim
Skim.*
Link Delays

## Slide 13: Microsimulator Applications
Version 4 Microsimulator
  Single thread, limited network/demand size  subarea applications
  Subarea polygon defines area for regional extraction
    SubareaNet and SubareaPlans
  Subarea link-delays merged with regional link-delays for feedback
Version 5 simulations
  Multiple cores (threads or MPI) processing multiple subareas
  Geographic subareas defined in the Node file using SimSubareas
    Normally the CBD is selected as the central subarea
      Lake Michigan makes subarea selection more challenging
    Subareas can be defined once or updated during each iteration based on link vehicle hours of travel (i.e., load balancing)

## Slide 14: Version 4 Microsimulator
LinkDelay
Regional Plans.*
PlanPrep
Time Plans
Regional Net
Regional Delays
Microsimulator
SubareaNet
SubareaPlans
Subarea Plans
Subarea Net
Subarea Delays
New Delays
Feedback

## Slide 15: Version 5 Microsimulator
Regional Plans.*
PlanPrep
Time Plans
Microsimulator
Regional Delays
SimSubareas
Regional Delays
Subarea Nodes
Feedback

## Slide 16: Microsimulator Feedback Loops
Microsimulator
Network
Travel Paths
Bottlenecks
Travel Times
Router
Trips / Tours
Change?
Change?
Stop
No
Yes
Yes

## Slide 17: Process Convergence

## Slide 18: Recent Convergence Discussions
Discussions with academics about Dynamic User Equilibrium (DUE) convergence using TRANSIMS
  New performance measures
  Link delay MSA averaging seems acceptable
  Less comfortable with selected traveler feedback
    Prefer simulating AON plans in each iterations
      Since a unique path is built for each trip, gridlock concerns may be minimized

## Slide 19: Equilibrium Statistics
AON Plans
Re-Skim Plans
AON Flows
Simulated Flows
Router
Trip File
Router
Plan File
Simulated Times
PlanCompare
LinkSum
Trip Gap
Relative Gap

## Slide 20: Equilibrium Convergence

## Slide 21: Trip Gap by Time of Day and Iteration

## Slide 22: Relative Gap by Time of Day and Iteration