## Slide 1: TRANSIMS Version 5 Network Files
January 20, 2011
David Roden – AECOM

## Slide 2: Topics
Overall goals and objectives
Major concept changes
File structure changes
New data fields and features
Presentation graphics

## Slide 3: Goal – Improved User Interface
Simplify editing
  Simplify the network coding requirements
  Reduce the number of coded dependencies between files
  Use data nesting to avoid sorting problems and record inconsistencies
Reduce user errors
  Standardize control keys and key definitions
    Directory and key names are the same as other files
    Key names are simplified and clarified
  Interpret user-provided unit specifications
    More intuitive/familiar units of measure (e.g., 25.3 mps = ??? mph)
  Simplify coding and editing

## Slide 4: Goal – More Advanced Applications
Enhance capabilities
  Coordinated signal timing and phasing plans
    Intersections coded with multiple nodes (e.g., divided arterials)
    Near-by signal coordination and traffic circles
  Metered or random vehicle processing rates by lane
    Toll plazas, ramp metering, security gates
  Vehicle type cost by lane and time of day
    HOT lanes and variable tolls
  Parking cost and access/egress times by time of day
    Parking lot choice
  Impact of vertical grades on truck speeds

## Slide 5: Major Concept Changes
Lane numbers and pocket lanes
Multi-node signals
Toll lanes and lane processing rates
Process links  access links
Link offsets

## Slide 6: File Structure Changes
Lane ranges
Link direction
  link-node  link-dir
Parking time period nests
Nested signal files
  Signal time periods, timing plans, and phasing plans
Transit schedules
  route-run-stop list  route-stop-run columns (i.e., time tables)

## Slide 7: New Data Fields
Node – subarea
Link – area type, grade, divided
Location – XY  link, offset, setback
Parking – time-in, time-out
Lane Use – toll, fixed and variable processing rates
Timing Plans – cycle length
Phasing Plans – movement
Detectors – use type

## Slide 8: Facility Type Numbers
Version 4  Version 5
1 = Freeway Freeway
2 = Expressway Expressway
3 = Principal Principal Arterial
4 = Major Major Arterial
5 = Minor Minor Arterial
6 = Collector Collector
7 = Local Local Thru
8 = Frontage Local
9 = Ramp Frontage Road
10 = Bridge Ramp
Version 4  Version 5
11 = Walkway Bridge
12 = Bikeway Tunnel
13 = Busway Other
14 = Light Rail Walkway
15 = Heavy Rail Bikeway
16 = Ferry Busway
17 = External Light Rail
18 = Heavy Rail
19 = Ferry
20 = External

## Slide 9: Lane Numbers
The link file no longer tracks pocket lanes
  Pocket lanes are numbered separately – L1, R1
Lanes are now numbered from right to left
  Greater consistency with other simulation packages and HCM
2
3
4
5
1
Link File:
3 thru lanes
1 left pocket
1 right pocket
Pocket File:
lane 1 turn
lane 5 turn
Version 4
Link File:
3 lanes
Pocket File:
1 right turn
1 left turn
3
2
1
R1
L1
Version 5

## Slide 10: Lane Number Usage
Impacted network and output files
  Link, Pocket, Lane-Use, Detector
  Lane Connectivity  Connection
  Problem, Snapshot, Occupancy
Lane coding
  Version 4: most files require separate records for each lane or lane combination
  Version 5: all files use lane ranges or lane range combinations
    Lane range examples: 1..3, R1..3, 3..L1, L1..L2, ALL
    Fewer records to edit, add, delete, sort
    Fewer coding errors and less time consuming
    Software builds and validates the lane relationships

## Slide 11: Lane Range Example – Lane Use
Limit all lanes to HOV in the AM Peak period
2
3
4
5
1
Lane Use Records:
Lane 1, HOV, period, etc .
Lane 2, HOV, period, etc.
Lane 3, HOV, period, etc.
Lane 4, HOV, period, etc.
Lane 5, HOV, period, etc.
Version 4
3
2
1
R1
L1
Lane Use Records:
Lanes ALL, HOV, period, etc.
or
Lanes R1..L1, HOV, period, etc.
Version 5

## Slide 12: Add a Pocket Lane in Version 4
Add a pocket lane to a link with parking restrictions
to
1
2
3
Link File:
3 thru lanes
0 left pocket
0 right pocket
Lane Use File:
Lane 3, closed, period 1
Lane 3, closed, period 2
Lane 3, closed, period 3
off-peak parking
2
3
4
1
off-peak parking
Pocket File:
lane 1 turn
Link File:
3 thru lanes
1 left pocket
0 right pocket
Lane Use File:
Lane 4, closed, period 1
Lane 4, closed, period 2
Lane 4, closed, period 3

## Slide 13: Add a Pocket Lane in Version 5
Add a pocket lane to a link with parking restrictions
to
3
2
1
Link File:
3 thru lanes
Lane Use File:
Lane 1, closed, period 1
Lane 1, closed, period 2
Lane 1, closed, period 3
off-peak parking
Pocket File:
1 left turn
3
2
1
L1
off-peak parking
Link File: (no change)
3 thru lanes
Lane Use File: (no change)
Lane 1, closed, period 1
Lane 1, closed, period 2
Lane 1, closed, period 3

## Slide 14: Link Connection Impacts
Version 4
  Lane numbers apply to both ends of the link
    Pocket lanes at one end impacts lane numbers at the other end
    Adding and deleting pocket lanes impacts all lane-related files
Version 5
  Lane numbers at each end are independent
    Pocket lane changes require relatively few network changes

## Slide 15: Version 4 Lane Connectivity Edits
1
2
3
2
3
4
1
1
2
3
Lane Connectivity:
Lane 1 to 1  Lane 1 to 2
Lane 2 to 2  Lane 2 to 3
Lane 3 to 3  Lane 3 to 4
Lane 1 to 3  Lane 1 to 4
Lane Connectivity:
Lane 1 to 1  Lane 2 to 1
Lane 2 to 2  Lane 3 to 3
Lane 3 to 3  Lane 4 to 2
Lane 3 to 1  Lane 4 to 1
1
1
1
2
3
1
2
3
1
2
3
1
1
add

## Slide 16: Version 5 Connection Edits
3
2
1
3
2
1
L1
3
2
1
Connection File:
Lane 1..3 to 1..3 (no change)
Lane 1 to 1 (no change)
Connection File:
Lane 1..3 to 1..3 (no change)
Lane 1 to 1 (no change)
1
1
3
2
1
3
2
1
3
2
1
1
1
add

## Slide 17: Link Offset
Link offsets are measured from the beginning of the link in the direction of travel
Version 4
  Network offsets are measured from the end of the link
  Microsimulator offsets are measured from the beginning of the link
Offset
Parking
Offset
Parking
Offset
Parking
Offset
Parking
Vehicle Offset

## Slide 18: Process Links  Access Link
Version 5 does not need Process Links
  Link-offsets are used to build direct two-way connections
  Access Links are only used for special connections
    Two-way or one-way links between nodes, locations, parking lots, and transit stops
Version 4.0
Parking
Activity
Location
2 one-way
Process Links
Version 5.0
Parking
Location
Location
Setback

## Slide 19: Access Link Options
Version 4 process links are required to connect
  activity locations  parking and activity locations  transit stops
Version 5 access links may connect
  locations  parking, locations  stops, locations  nodes
  locations  locations, stops  stops, nodes  nodes
  parking  stops, parking  nodes, stops  nodes
Walk links with travel time, distance, and cost
Transit stops no longer need activity locations
  Activity locations with a zero zone number are deleted

## Slide 20: Lane Use File
Version 5 differences
  Lane ranges, direction code, offsets, length units
Version 4 toll file  Version 5 lane use file
  Enables tolls by lane (e.g., HOT lanes)
Lane processing rate added
  Fixed and variable/random vehicle delays
  Toll plazas, ramp metering, security gates

## Slide 21: Parking File
Nested record structure
  Single and unique parking lot location – link-offset and type
Time-of-day and use/vehicle type nests
  Variable parking costs
  Access and egress times (~terminal time)
    Time required to park or un-park the vehicle
  Parking spaces
    Shadow prices or access time can be used to model capacity constraints

## Slide 22: Traffic Signals
Signalized node  signal controller
  Four cross-referenced files
    Signal, Timing Plan, Phasing Plan, Detector
    Signal Coordinator file dropped
Primary differences
  Multi-node signal coordination
  Re-usable timing and phasing plans
  Barrier, ring, and position codes
    Greater compatibility with traffic signal software
  Detectors include use types (e.g., buses or trains)
  Nested file structures for tighter record management and fewer coding errors

## Slide 23: Multi-Node Signal Controllers

## Slide 24: Traffic Circles

## Slide 25: Divided Roadways

## Slide 26: Signal File
Version 5 differences
  Node  controller number
    Controls a list of nodes
  Nested time period records (with end times)
    Improve record management and minimize coding mistakes
  Re-useable timing and phasing ID numbers
Signal | Group | Times | Nodes
Start | End | Timing | Phasing
1 | 2 | 5 | 101¦102¦103
0:00 | 6:00 | 1 | 1
6:00 | 9:30 | 2 | 1
9:30 | 16:00 | 1 | 1
16:00 | 19:00 | 3 | 1
19:00 | 27:00 | 1 | 1

## Slide 27: Timing Plan File
Version 5 differences
  Controller number + timing ID indexing
    Signal type (timed/actuated), offset, and cycle length
  Nested phase records
    Improve record management and minimize coding mistakes
  Barrier, ring, and position codes
    Clearer sequencing and improved linkages to traffic signal software
Signal | Timing | Type | Cycle | Offset | Phases | Notes |  | 
Phase | Barrier | Ring | Position | Min_Green | Max_Green | Extension | Yellow | All_Red
1 | 1 | Actuated | 100 | 0 | 4 | 0:00..6:00 |  | 
1 | 1 | 1 | 1 | 5 | 5 | 0 | 0 | 0
2 | 1 | 1 | 2 | 20 | 39 | 12 | 3 | 1
3 | 1 | 1 | 3 | 5 | 9 | 3 | 0 | 0
4 | 1 | 1 | 4 | 20 | 39 | 12 | 3 | 1

## Slide 28: Phasing Plan File
Version 5 differences
  Node  controller number and direction code
    Multi-node signals and cross-referencing
  Nested movements records
    Improve record management and minimize coding mistakes
  Movements descriptions
    User help and improved linkages to traffic signal software
Signal | Phasing | Phase | Movements | Detectors
Movement | Link | Dir | To_Link | Protection
1 | 1 | 1 | 4 | 1¦3
EB_Left | 4892 | 1 | 3164 | Protected
WB_Left | 4202 | 0 | 439 | Protected
NB_Right | 439 | 0 | 4202 | Stop_Permit
SB_Right | 3164 | 1 | 4892 | Stop_Permit

## Slide 29: Detector File
Version 5 differences
  Node  direction code
  Offset from the beginning of the link (meters/feet)
  Lane ranges with pocket lane codes
  Use types
  No signal coordinator
Detector | Link | Dir | Offset | Length | Lanes | Type | Use | Notes
1 | 4892 | 1 | 1043.5 | 30 | L1 | Presence | Any | Left Turn
2 | 4892 | 1 | 1043.5 | 30 | R1..2 | Presence | Any | Thru Right
3 | 4202 | 0 | 1137.9 | 30 | L1 | Presence | Any | Left Turn

## Slide 30: Presentation Graphics
ArcNet with curved connections
Version 4
Version 5